## Slide 1
Imperial College London
World-Frame Pose Hold for a Torso-Mounted SRL
Week 4: reactive baseline restored, instrumented, and quantified
Christian · MUVE Lab · weekly supervisor meeting · 10 July 2026
Context. Phase 1 of the thesis pipeline: the strongest possible reactive baseline in MuJoCo (dual Kinova Gen3, world-frame task), against which predictive control will later be measured.
Notes: TIME 0:30 (cumulative 0:30). OBJECTIVE: frame the week. KEY MESSAGE: this week turned a broken controller into a measured baseline with numbers that can go in the thesis. Say: research question is whether predictive control beats reactive under human-induced base motion; the comparison is only valid if the reactive baseline is strong, so week 4 was about making the baseline real and measurable. Do not linger; move to achievements. NOTE: replace the text wordmark on every slide with the official Imperial logo asset before presenting.

## Slide 2
Imperial College London
This week: a measured baseline
Every change serves one goal: a baseline strong enough that the later predictive comparison means something.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
2
Controller
Tracking performance restored and pinned against last known-good behaviour
Pure control math split from MuJoCo plumbing: control loop explicit, portable to C++
Pinocchio FK sensing path: EE pose composed from torso pose + joint angles, never read from MuJoCo: mirrors Vicon + encoders on hardware
Null-space joint centering added (redundancy resolution, K_NULL)
Evidence infrastructure
Reproducible experiment runner: every run saves metrics.json keyed to git commit
Staged gain-sweep tool (4 stages, disqualification guards, resumable)
13 test modules, incl. FK checked against MuJoCo direct readings as ground truth
Git discipline: each verified change is one commit; behaviour diffs traced to code diffs
Notes: TIME 1:00 (cumulative 1:30). OBJECTIVE: show progress is technical, not just coding. KEY MESSAGE: the left column is the controller, the right column is what makes claims about it checkable. Emphasise cause and effect: the FK sensing path exists so the sim controller sees the same information the hardware will (Vicon torso pose + encoders), which keeps the C++ port honest. The runner keying metrics to commits is why every number later in this talk is reproducible. LIKELY QUESTION: 'what broke and why?': answer: a frame/composition regression; recovered by diffing against the last working commit rather than re-tuning gains.

## Slide 3
Imperial College London
Controller architecture
One explicit kinematic loop on position servos: no dynamics inversion, every stage traceable and portable to C++.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
3
Inputs (world frame)
target mocap pose + joint angles q, base twist
Forward kinematics
T_W_E = T_W_T · T_T_K · T_K_E(q) (Pinocchio)
Pose error
e = ref − actual; e_rot = axis-angle of R_ref·R_eeᵀ
Twist command
v = Kp·e + Kd·e_v [m/s; rad/s], linear-first
Damped least squares
qdot = Jᵀ(JJᵀ+λ²I)⁻¹v + null-space centering
Outputs
ctrl += qdot·dt → MuJoCo position servos
Sensing contract. The EE pose is never read from the simulator in the control path: it is composed from the torso pose (future: Vicon) and arm FK (future: encoders). Integrating servo setpoints (ctrl += qdot·dt) makes qdot = 0 the fixed point, so gravity droop is compensated for free.
Notes: TIME 1:15 (cumulative 2:45). OBJECTIVE: explain how the controller works, inputs to outputs. KEY MESSAGE: it is a deliberately simple, explicit loop; simplicity is a feature for the C++ port and for attributing failures. Walk the boxes in order: inputs, FK composition, world-frame pose error, P/PD twist law, DLS with null-space centering, setpoint integration into position servos. All SI units internally; mm only at plot boundaries. LIKELY QUESTIONS: 'Why not torque control?': Gen3 exposes a position/velocity interface and kinematic control is safer around a human wearer; dynamics-level control is future work. 'Why DLS?': bounded qdot near singularities at the cost of tracking bias, lambda = 0.043 from the sweep. 'Why world-frame error?': the task is a world-frame pose hold; a torso-frame reference would hide exactly the disturbance we are trying to reject.

## Slide 4
Imperial College London
Performance under base sway
Stable, arm-symmetric pose hold, but reactive rejection is weak: the error tracks the base motion with lag.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
4
126 mm
position RMSE (per arm)
262 mm
peak position error
0.55 deg
rotation RMSE
12.7 %
peak-error rejection vs base
FIGURE
analysis/output/base_vs_error.png
Base displacement vs EE error norm, both arms: shows error locked to base phase with lag
Scenario
±0.3 m x-sway at 0.1 Hz (peak 0.19 m/s), 25 s evaluation after settling, both arms controlled
Left/right arms agree within 1% on every metric: no asymmetry in the contact-free case
Velocity saturation < 0.5% of cycles; zero contacts in this scenario
Notes: TIME 1:15 (cumulative 4:00). OBJECTIVE: give the honest headline numbers. KEY MESSAGE: the controller holds pose stably, but a pure-feedback loop at this bandwidth only removes ~13% of the peak disturbance at 0.3 m amplitude: that gap is the thesis opportunity, not an embarrassment. Define the metric before anyone asks: rejection = 1 − (peak EE error / peak base displacement). Errors are world-frame norms; e = ref − actual. Numbers are the stage-4 sweep winner run, commit-keyed. LIKELY QUESTIONS: 'Is 126 mm not terrible?': at 0.3 m amplitude the untracked error would be ~300 mm; the point is to characterise the reactive ceiling, and rejection improves at smaller amplitude/frequency (bandwidth sweep exists as backup). 'Why peak-based rejection?': acknowledged limitation, frequency-domain characterisation is next week.

## Slide 5
Imperial College London
Staged gain sweep: tuning is saturated
Tuning halved rotation error but moved position RMSE by <2%: the residual error is lag, not gain.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
5
FIGURE
analysis/output/gain_sweep/sweep_progression.png
Stage-by-stage metric progression (pos gains → rot gains → scale → damping/null); heatmaps in backup
Gain | Winner
KP_POS [1/s] | 1.81
KP_ROT [1/s] | 6.52
KD_POS / KD_ROT [–] | 0.9 / 0.9
K_NULL [1/s] | 2.0
DLS λ [–] | 0.043
What it changed
Rotation RMSE: 1.08° → 0.55° (halved)
Position RMSE: 127.6 → 125.6 mm (−1.6%)
Stages 3–4: no candidate beat the guard thresholds: the position plateau is structural (feedback lag), which is exactly what predictive control should attack
Notes: TIME 1:00 (cumulative 5:00). OBJECTIVE: show the tuning was systematic and interpret its outcome. KEY MESSAGE: gains are no longer the bottleneck; the position-error plateau under sweep is evidence the reactive architecture, not its tuning, limits rejection: this is the empirical setup for the predictive phase. Method in one breath: four sequential stages (position gains grid, rotation gains grid, uniform scale, damping + null gain), each stage inherits the previous winner; candidates disqualified on explicit guards (settling, saturation, joint-margin, rotation-RMSE regression); all runs commit-keyed and resumable. LIKELY QUESTIONS: 'Sequential sweeps miss gain coupling': true; accepted trade for a solo builder, and the scale stage partially probes coupling. 'Why is KD so high (0.9)?': the D-term feeds forward a fraction KD/(1+KD) of base velocity, trading settle speed for rejection; measured, not hand-waved.

## Slide 6
Imperial College London
Limitations and failure analysis
The dominant failure is mechanical, not mathematical: under torso roll, the right arm collides with the torso.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
6
FIGURE
analysis/output_nocontact/A_failure_story.png
Failure-story figure: right-arm error vs roll phase with contact onset marked (diagnosis scenario: 0.1 m sway + 23° roll)
Contact failure (diagnosed, not guessed). 23° torso roll → right arm–torso contact in 77% of steps; error grows 20 → 200–320 mm on positive-roll half-cycles; servo lag hits 2.7 rad. Controller has no contact awareness. Left arm: zero contacts, tracks throughout.
Joint limits. Joint 6 camps on its position limit on both arms; DLS has no limit-avoidance term.
Singularity at start-up. The model's home configuration is rank-3 (σ_min ≈ 0); convergence relies on the transient escaping it.
Assumptions. Perfect state, zero latency, kinematic control (dynamic coupling ignored), scripted single-axis sinusoids only, peak-based rejection metric.
Notes: TIME 1:15 (cumulative 6:15). OBJECTIVE: critically analyse the controller like a researcher. KEY MESSAGE: I know exactly why it fails and can prove it: the diagnosis separated contact from singularity by phase analysis (conditioning dips at negative roll extremes, error peaks at positive extremes; sigma_min statistically identical between the healthy and failing arm). Be explicit that the initial error rise ~1 s before first touch is bandwidth lag, not contact: shows the diagnosis is honest about what contact does and does not explain. LIKELY QUESTIONS: 'Why not just add collision avoidance now?': next week, via task placement + null-space posture first, because that isolates the mechanical failure without confounding the baseline's control law. 'Does the singular home config matter on hardware?': hardware will not start at the zero configuration; still flagged because it pollutes start-up metrics.

## Slide 7
Imperial College London
Next week
Priority order: remove the dominant failure mode, then make the evidence thesis-grade.
MUVE Lab · MSc project · Week 4 · 10 Jul 2026
7
1
Collision-aware task placement
Re-site task poses + bias null-space posture away from the torso; re-run the roll scenario. Success: zero contact occupancy, right arm matches left.
2
Disturbance realism
Multi-axis sway + roll; amplitude/frequency grid → rejection-vs-frequency curve. This quantifies the reactive bandwidth ceiling the thesis argues against.
3
Metric hardening
Frequency-domain rejection (not peak-only), settle criteria tightened, per-axis error reporting for the thesis plots.
4
Validation depth
Extend ground-truth checks (velocity path already validated against finite differences) to the error and DLS stages.
Deliverable at next meeting
Rejection-vs-frequency plot and a collision-free repeat of this week's scenario, same commit-keyed pipeline.
Deliberately deferred
Predictive/MPC work, C++ port, visualisation polish: out of scope until the baseline is defensible.
Notes: TIME 0:45 (cumulative 7:00). OBJECTIVE: show a prioritised, falsifiable plan. KEY MESSAGE: item 1 removes the failure that dominates every metric; item 2 produces the single figure the thesis comparison will hang on. Each item has a success criterion, so next week's meeting can check them off. Close by inviting steer: does the supervisor want orientation-control refinement promoted above metric hardening? LIKELY QUESTIONS: 'When does predictive work start?': once the rejection-vs-frequency curve exists, because that curve is the baseline the predictive controller must beat. 'Hardware timeline?': C++ port begins after the reactive baseline is frozen; nothing in the control path is Python-only by design.